## Slide 1: Identifying TRAFFIC Congestion Precursors Using Machine Learning Methods
Nishu Choudhary
Dr. Angshuman Guin & Dr. Michael P. Hunter
March 2022

## Slide 2: Overview
Motivation-Problem overview
Site Description
Problem Formulation
Dataset Filtering
Machine Learning Classifiers
Results
Limitations and Future Directions

## Slide 3: Motivation
Current Practices –reactive to traffic state
Prediction Model- allow traffic management agencies to take preemptive actions
Ramp Metering: Maryland’s I-270
Source: https://wjla.com/news/local/flashing-yellow-lights-maryland-ramp-metering-system-i-270
Dynamic Message Sign: WSDOT
Source: https://wsdot.wa.gov/travel/operations-services/active-traffic-and-demand-management
Variable Speed Limit: WSDOT
Source: https://wsdot.wa.gov/travel/operations-services/active-traffic-and-demand-management

## Slide 4: Background
Recurring congestion- spatiotemporal patterns1
Non-recurring congestion- incident, weather1
Identify precursor for imminent traffic congestion
Previous studies- regression based prediction traffic flow, speed or travel time2
1.Jessica McGroarty, Recurring and non-recurring congestion: Causes, impacts, and solutions. Neihoff Urban Studio–W10, University of Cincinnati (2010)
2. Nishant Kumar, Martin Raubal, Applications of deep learning in congestion detection, prediction and alleviation: A survey, Transportation Research Part C: Emerging Technologies, Volume 133, 2021, 103432, ISSN 0968-090X, https://doi.org/10.1016/j.trc.2021.103432.

## Slide 5: Site Description-1
Data by © OpenStreetMap, under ODbL
3954
3953
3950
3945
3940
3935
3930
N
I85 Freeway section: From Buford Hwy Exit to Clairmont Rd. NE
Northbound Direction
Video Detection System Device IDs [3930-3940]

## Slide 6: Site Description-2
N
N
Recurrent Bottleneck
Direction of travel
Data by © OpenStreetMap, under ODbL
04/24/2018
Average speed (mph.) for I-85 freeway section on 04/24/2018

## Slide 7: Recurrent Bottleneck
04/12/2018
04/18/2018
04/10/2018
Average speed (mph.) for I-85 freeway section

## Slide 8: Problem Formulation
Average speed (mph.) over 1-min for the selected freeway section on 04/04/2018
Discard the data
Speed drop detected in the section
Label Zero
Last 5-minutes: Label One
Pre-congestion period 6 min to 31.5 min3
3.Persaud B, Yagar S, Brownlee R. Exploration of the Breakdown Phenomenon in Freeway Traffic. Transportation Research Record. 1998;1634(1):64-69. doi:10.3141/1634-08

## Slide 9: Dataset Filtering
Rules:
Remove congestion events where bottleneck is located outside the site [3940-3930]
Incident related congestion events removed from data. But, if the start time of an incident later than start of congestion, include the event
Exhibit for Rule #1
Exhibit for Rule #2
Incident

## Slide 10
Incident cross-check
Devices denoted by black markers
Incidents: other colors
Accident = Red
Stall = Light-green
Debris = Beige
Event ID
Start-time

## Slide 11: Machine Learning Classifiers
Discriminative: estimate the decision boundary
Generative: model joint probability distribution
Support Vector Machines4
Source:https://towardsdatascience.com/support-vector-machine-simply-explained-fee28eba5496
Naïve Bayes Classifier5
Source: Davenport, 2022
Tree-based: break input space into regions
Neural Network: feedforward network to approximate a function
Neural Network7
Source: Lan, 2020
Decision Trees6
Source: Lan,2020
Random Forest6
Source: Lan,2020
Notes: 4. https://towardsdatascience.com/support-vector-machine-simply-explained-fee28eba5496
5. Dr. Mark Davenport, MD. (2022, February 16). Logistic Regression and Naïve Bayes . Electrical and Computer Engineering, Georgia Institute of Technology. https://mdav.ece.gatech.edu/ece-6254-spring2022/notes/10-LR-NB.pdf
6. Dr. George Lan, GL. (2020, April 28). Decision Trees and Random Forest. Industrial and Systems Engineering, Georgia Institute of Technology
7. Dr. George Lan, GL. (2020, March 16). Neural Networks-Lecture#13. Industrial and Systems Engineering, Georgia Institute of Technology.

## Slide 12: Results
March | 11 days
April | 15 days
May | 18 days
Training | 36 days
Testing | 8 days
Class Distribution |  | 
Training | {‘1’: 180 ‘0’: 17396} | 1.02%
Testing | {‘1’: 40 ‘0’: 3510} | 1.13%
Original Labeling 05/25/2018
Predicted Labeling 05/25/2018
Label: zero
Label: one
Predicted Label: zero
Predicted Label: one

## Slide 13: Results
Machine Learning Classifier | Accuracy | Recall | Precision
SVM-polynomial Kernel | 0.61 | 0.23 | 0.26
SVM-Radial Kernel | 0.61 | 0.23 | 0.33
Neural Network | 0.58 | 0.18 | 0.23
Decision Tree Classifier | 0.90 | 0.90 | 0.10
Random Forest Classifier | 0.96 | 1.00 | 0.14
Naive Bayes classifier | 0.94 | 1.00 | 0.09
March | 11 days
April | 15 days
May | 18 days
Training | 36 days
Testing | 8 days
Class Distribution |  | 
Training | {‘1’: 180 ‘0’: 17396} | 1.02%
Testing | {‘1’: 40 ‘0’: 3510} | 1.13%
Recall Score8 =
Precision Score8 =
Notes: 8. Scikit-learn: Machine Learning in Python, Pedregosa et al., JMLR 12, pp. 2825-2830, 2011.

## Slide 14: Limitations & Future Directions
Increase the dataset size
Explore Deep Learning models
Thank you for your time
Contact: nishuchoudhary@gatech.edu